## Slide 1
Task definition
IEEE student contest 2021
Task definition
rearrange the network to maximize the settling time
Settling Time if voltage ±2% of static voltage
All ECUs need to be used
ECUs must be separated by at least one line

## Slide 2
First Principle Approach Transmission line basics
Reflection coefficient
Z2 | Γ
0 | -1
Z1 | 0
∞ | 1
Guidelines for bad circuit
Increasing reflection coefficient
Avoid matching
Longest transmission lines paired with the worst reflection coefficient
After applying the rules:

## Slide 3
First Principle Approach
Wave propagation example
1
0,333
1.334V
1.334V
1.334V
1.334V
1

## Slide 4
First Principle Approach Compare both circuits
Best circuit (given)
First principle approach circuit

## Slide 5
This took way more time than was necessary Brute Force Approach
0-4 transmission lines
{ECU1, ECU2, ECU3, ECU4}
Netlists of all allowed circuits
Generation
Simulation
Circuit netlist
Simulation parameters
Maximum settling time
Post-Processing
Circuit parameters
Simulation results
Find worst circuit

## Slide 6
Generation Overview
0-4 transmission lines
{ECU1, ECU2, ECU3, ECU4}
Netlists of all allowed circuits
Generation
Graph
Topology
Circuit
To Simulation

## Slide 7
Generation Graphs

## Slide 8
Generation Graphs to Topology
Graph Elements
Edges = TLs
Vertices
  Connect TLs
  Integrate Devices
  Different configurations possible
Topology Elements
Transmission Lines
Devices

## Slide 9
Generation Vertices
Vertex Type 1
Allowed connections
Open circuit
Short circuit
Connected device

## Slide 10
Generation Vertices
Vertex Type 2
Allowed connections:
Short circuit
Connected device
Allowed connections:
Open circuit
Connected device

## Slide 11
Generation Vertices
Vertex Type 3a
Allowed connections:
Short circuit
Connected device
Allowed connections:
Open circuit
Connected device

## Slide 12
Generation Vertices
Vertex Type 3b
Allowed connections:
Short circuit
Connected device
Allowed connections:
Open circuit
Connected device

## Slide 13
Generation Vertices
Vertex Types 4a, b, c

## Slide 14
Generation Graph to Topology
All possible topologies for graph
One topology configuration for graph
Get all allowed topologies
Build topology

## Slide 15
Generation Graph to Circuit
One topology configuration for graph
Assign ECUs to devices
Assign TL values to TLs
One circuit configuration for topology

## Slide 16
Generation Circuits
Graph | topology configs | parameter configs | total configs
P3 | 1 | 288 | 288
P4 | 39 | 576 | 22 464
P5 | 330 | 576 | 190 080
K3 | 30 | 576 | 17 280
K2,2 | 195 | 576 | 112 320
K1,3a | 84 | 576 | 48 384
3-PANa | 424 | 576 | 244 224
CHAIRa | 717 | 576 | 412 992
K1,4a | 1 089 | 576 | 627 264
 |  |  | Total 1 675 296

## Slide 17
Brute Force Approach
0-4 transmission lines
{ECU1, ECU2, ECU3, ECU4}
Netlists of all allowed circuits
Generation
Simulation
Circuit netlist
Simulation parameters
Maximum settling time
Post-Processing
Circuit parameters
Simulation results
Find worst circuit

## Slide 18
Simulation
Simulation to Settling Time
PySpice
PySpice -> Python Library interface with NgSpice (API)
NgSpice -> open-Source fork of Spice
  allows a programmatic approach for simulation
Determine Settling Time
Simulate circuit
Find static value for every node
Fine the last point where voltages exceed threshold +/- 2 %
Save node configuration, settling time and plot
​

## Slide 19
Brute Force Approach
0-4 transmission lines
{ECU1, ECU2, ECU3, ECU4}
Netlists of all allowed circuits
Generation
Simulation
Circuit netlist
Simulation parameters
Maximum settling time
Post-Processing
Circuit parameters
Simulation results
Find worst circuit

## Slide 20
Results Circuit 3-PANa_nlC037_pC156
Settling time: 64.89µs
Somewhat unintuitive…
Not plausible?
???

## Slide 21
Results Circuit 3-PANa_nlC275_pC243
Settling time: 1.34µs
But actually 180ns…

## Slide 22
Results Circuit P5_nlC247_pC034
Settling time: 0.93µs
Not sure if parallel ECUs ok
But actually 7.4µs !

## Slide 23
Results Circuit P5_nlC247_pC034_mod03
Settling time: 7.4µs

## Slide 24
Conclusions
Generation Problems
Not all circuits plausible
Very complicated
Simulation Problems
Diverging nodes
Unfamiliar library
Settling time detection faulty
Lessons learned…
First principle approach is viable
Simulations can be misleading
Physical understanding improves simulations
node.py
port.py
nodeLink.py
transLine.py
vertex.py
graph.py
Notes: Problems simulation side
Simulation Error : "step time to small"
Simulation timeouts without Error massage
  Prevented continuous simulation
Divergence of static nodes
  static voltage more difficult
Settling detection is faulty

## Slide 25
Thank you for your attention
Cem Gülsan
cem.guelsan@tuhh.de
Valentin Resapow
valentin.resapow@tuhh.de
GitHub:
valli96/IEEE_student_contest_2021
Conclusions

## Slide 26
node.py
port.py
nodeLink.py
transLine.py
vertex.py
graph.py

## Slide 27
This took way more time than was necessary PySpice Simualtion
Circuit simulation
Determine Settling time
Save simulation plot & data
Circuit simulation
nlConfigs
paramConfigs
Graph
handover to simulation (parsing)
Find longest time
Determine corresponding circuit
Verify with LTSpice
Generation
Simulation
Post processing

## Slide 28
Generation Graphs

## Slide 29
Typ 1
Typ 2
Typ 3a
Typ 3b

## Slide 30
Typ 4a
Typ 4b
Typ 4c

## Slide 32
Typ 1
Typ 2
Typ 3a
Typ 3b

## Slide 33
Typ 4a
Typ 4b
Typ 4c

## Slide 39
Click to add text

## Slide 40
Intro
  Task
First Principle Approach
  TL basics
  Applying TL basics
  Worst circuit
  Comparison
Brute Force Approach
  General